## Slide 1: Hotel Network Infrastructure Design Using Cisco Packet Tracer
Presented by:
Hotel Network Topology
Abdul Rafay (Roll No: 243705)
Subject: Computer Network
Submitted To: Mr. Mohammad Azam
Section: Bs Cyber Security – A

## Slide 2: Project Overview
This project presents the design of a secure and scalable hotel network.
The network is implemented using Cisco Packet Tracer.
It supports wired and wireless users across multiple hotel departments.

## Slide 3
Project Objectives

## Slide 4
Network Architecture

## Slide 5
Security & Traffic Control

## Slide 6
Complete Network Topology
This topology represents the complete hotel network layout.

## Slide 7
VLAN Design & Segmentation

## Slide 8
VLAN & IP Addressing Scheme:
Each VLAN uses a separate /24 subnet.
Default gateways are configured on Core Switch SVIs.

## Slide 9
What we use in Our Network System.

## Slide 10
Core Infrastructure & Switching Technologies
LAN (Local Area Network):
  Integrated Admin, Guest Rooms, and Parking into a unified campus network.
VLAN (Virtual LAN):
  Created 9 VLANs (e.g., VLAN 10 Parking, VLAN 60 Rooms) for traffic segmentation .
L3 Switch (Layer 3 Switch):
  Deployed Cisco Catalyst 3560 as the Core Backbone for high-speed packet processing .
Inter-VLAN Routing:
  Enabled on the Core Switch to allow secure communication between departments.
LAN Switching:
  Used Cisco 2960 Access Switches for floor-level distribution.
Network Core & Switching Architecture

## Slide 11
Security, Edge & WAN Implementation
Network Security & External Connectivity
ASA (Adaptive Security Appliance):
  Implemented Cisco ASA 5506-X Firewall for stateful traffic inspection.
ACL (Access Control List):
  Applied VLAN-CONTROL to block Guest VLANs from accessing Management Servers .
NAT & PAT:
  Configured Dynamic NAT/PAT to mask internal private IPs behind a single Public IP (203.0.113.2).
WAN & ISP:
  Established a WAN link connecting the Firewall to the ISP Router (203.0.113.1).

## Slide 12
Protocols, Services & Operations
IP Addressing, Protocols & Services
IPv4 & IP:
  Designed a hierarchical 192.168.x.x addressing scheme for device identification .
DHCP (Dynamic Host Configuration Protocol):
  Centralized server for automated IP assignment to Staff and Guests .
DNS (Domain Name System):
  Mapped security.safari.com to the IoT Server for ease of access.
Transport & Diagnostics:
  TCP/UDP: Used for reliable Web/DNS traffic.
  ICMP: Enabled for connectivity testing and troubleshooting (Ping).
PC (Personal Computer):
  End-user terminals deployed in Reception and Admin offices.

## Slide 13
Firewall (ASA 5506) Implementation
Firewall separates internal network from ISP.
NAT (PAT) configured for internet access.
Traffic inspection policies enabled.

## Slide 15
CABLE
CONNECTIONS:

## Slide 22
CONFIGRATIONS:

## Slide 24
Access Switch Configuration
Access ports assigned to appropriate VLANs.
802.1Q trunk links toward core switch.
Port security applied to limit unauthorized devices.

## Slide 25
Access Switch Configuration
For Floor 2:

## Slide 26
For Wireless Device Connectivity

## Slide 27
Core Switch Configuration

## Slide 28
Core Router Configuration
Static routing implemented.
Routes internal VLAN traffic toward core switch.
Default route points toward firewall.
Static iP Addressing applied successfully!!

## Slide 29
Core Router Running Configuration (CORE-RTR)
!
version 15.1
no service timestamps log datetime msec
no service timestamps debug datetime msec
no service password-encryption
hostname Router
ip cef
no ipv6 cef
interface GigabitEthernet0/0
ip address 10.0.0.2 255.255.255.252
duplex auto
speed auto
interface GigabitEthernet0/1
ip address 10.0.0.5 255.255.255.252
duplex auto
speed auto
interface GigabitEthernet0/2
shutdown
ip classless
ip route 192.168.0.0 255.255.0.0 10.0.0.1
ip route 0.0.0.0 0.0.0.0 10.0.0.6
!
end

## Slide 30
Firewall (ASA 5506) Implementation

## Slide 33
Network Testing & Verification
Ping tests verify inter-VLAN connectivity.
End devices successfully access servers and internet.
We contacted a PC from Guest-Lounge having ip-Address: 192.168.0.10
from our main IT System PC and it was successful:

## Slide 34
Internal Network to Isp:
Firewall Log:
Ping test: From our Admin Device To ISP Router and it was successful:
Result:
Firewall Block Generate the Log.

## Slide 35
ISP To Internal Network :
Ping test: From ISP Router To our Internal Netrork and it was
Blocked By the Firewall
Result:
Firewall Block The outsite Trafic
Ping 192.168.10.1

## Slide 36
Conclusion:

## Slide 37
Questions